SECTION

MASTER FORMAT 1995 - 10510

MASTER FORMAT 2004 - 10 51 43

WIRE MESH LOCKERS

NOTE TO USER: This document contains instructions in red hidden text.  If this text is not visible MS WORD users may turn it on by clicking Tools, Options, going to the View Tab, and checking the Hidden Text box under the Formatting Marks section, then Click OK.  The instructions should appear. Users of other word processors may download the Three Part Spec without hidden text, and see the instructions in Bold black type.

** NOTE TO SPECIFIER **  WireCrafters; storage lockers.

This section is based on the products of WireCrafters, LLC, which is located at:

6208 Strawberry Lane

Louisville, KY  40214-2900

Tel: (800) 626-1816

Tel: (502) 363-6691

Fax: (502) 361-3857

www.wirecrafters.com

WireCrafters' solid steel and woven wire storage lockers are ideal for secured storage areas in large rooms or under utilized areas, where lockers will add efficiency to the storage area, secure stored items, and eliminate clutter.  WireCrafters also makes traditional partitions, industrial barriers to separate work areas, railings to enclose open sides of mezzanines, and wire mesh enclosures for pallet racks, which are not included in this section.

GENERAL

SECTION INCLUDES

Wire mesh storage lockers

Solid sheet metal bulk storage lockers.

RELATED SECTIONS

** NOTE TO SPECIFIER **  Delete any sections below not relevant to this project; add others as required.

Section 09900 - Paints and Coatings:  Field painting.

SUBMITTALS

Submit under provisions of Section 01300.

Product Data:  Manufacturer's printed data on products to be furnished.

Shop Drawings:  Complete layout and fabrication drawings.

Samples:  Finish color samples for selection.

Keys:  Turn over keys for door locks to Owner at completion of project.

PRODUCTS

MANUFACTURER

Acceptable Manufacturer:  WireCrafters, LLC; 6208 Strawberry Lane, Louisville, KY  40214-2900.  ASD.  Tel: (800) 626-1816 or (502) 363-6691.  Fax: (502) 361-3857.  www.wirecrafters.com  Email: info@wirecrafters.com

** NOTE TO SPECIFIER **  Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

Substitutions:  Not permitted.

Requests for substitutions will be considered in accordance with provisions of Section 01600.

STORAGE LOCKERS

Storage Lockers:  Factory-assembled modular sized door and divider panels bolted together, complete with all components, accessories, hardware, and fasteners; interchangeable units that allow expansion without waste of components.

** NOTE TO SPECIFIER **  Delete two of the following three paragraphs.

Style:  Single tier.

Style:  Double tier.

Style:  Single and double tier, in arrangement shown on drawings.

** NOTE TO SPECIFIER **  Delete two of the following three paragraphs.

Width:  36 inches (915 mm).

Width:  48 inches (1220 mm).

Width:  _________________

** NOTE TO SPECIFIER **  Delete three of the following five paragraphs.

Depth:  36 inches (915 mm).

Depth:  48 inches (1220 mm).

Depth:  60 inches (1524 mm).

Height:  90 inches (2286 mm).

Height: ___________________

** NOTE TO SPECIFIER **  The following three paragraphs are optional.

Provide tops of same construction as panels.

Provide backs where lockers are not to be installed against a wall; 20 gauge galvanized steel sheet.

Provide formed steel sheet bottoms.

Finish:  Electrostatic sprayed enamel, in manufacturer's standard color.

Provide appropriate hardware for fastening panels together and anchoring in place.

** NOTE TO SPECIFIER ** Delete either B. or C. below.

Wire Mesh Panels:  Steel angle frames with wire mesh securely welded in place; factory drilled holes for fasteners.

Wire Mesh:  10 gauge, 0.135 inch (3.5 mm) steel wire woven into 1 by 2 inch (25 by 50 mm) rectangular mesh.

Door Frames:  1-1/4 by 1-1/4 by 1/8 inch (32 by 32 by 3 mm) hot rolled steel angle.

Wall Frames:  1-1/4 by 1-1/4 by 1/8 inch (32 by 32 by 3 mm) hot rolled steel angle on three sides, 1/8 inch by 3 inch (3 mm by 76 mm), steel flat on fourth side.

Single Tier Doors:  1/4 by 3/4 inch (6 by 19 mm) steel bar stiffener securely welded to frame behind mesh.

Doors:  Factory pre-hung; 2-1/2 by 2-1/2 inch (63 by 63 mm) spun pin hinges, welded in place; door strike and padlock hasp.

Solid Sheet Metal Panels:  Steel angle frames with sheet metal securely welded in place; factory drilled holes for fasteners

Sheet Metal: 16 gauge 0.0598 inch hot rolled sheet

Door Frames:  1-1/4 by 1-1/4 by 1/8 inch (32 by 32 by 3 mm) hot rolled steel angle.

Wall Frames:  1-1/4 by 1-1/4 by 1/8 inch (32 by 32 by 3 mm) hot rolled steel angle on three sides, 1/8 inch by 3 inch (3 mm by 76 mm), steel flat on fourth side.

Single Tier Doors:  1/4 by 3/4 inch (6 by 19 mm) steel bar stiffener securely welded to frame behind mesh.

Doors:  Factory pre-hung; 2-1/2 by 2-1/2 inch (63 by 63 mm) spun pin hinges, welded in place; door strike and padlock hasp.

Optional Three Point Locking system.

Dividers and Bottoms:  16 gauge galvanized steel sheet, formed to provide extra strength and rigidity.

Dividers:  Anchor to supports bolted to wall panels, at 45 inches (1143 mm) above floor.

EXECUTION

INSTALLATION

Install in accordance with manufacturer's instructions.

Install plumb, level, and securely anchored to floor and to other structural members where indicated, shim where necessary.

Adjust doors smooth, easy operation.

END OF SECTION